## Slide 1: The Complete RFID Solution
Total Hospital Access Control, Tracking, & Asset Management

## Slide 2: RFID - what are the components?
RFID tag
Active & Passive RFID tags respond to readers with unique IDs:
Host System
RFID Reader
RFID Tags
Chip
Antenna
Packaging or substrate
RFID Middleware
enterprise Integration

## Slide 3: Active Technology
Components
Reader
  Listens for Tag beacons, can call individual tags
  Programs tags with ID and how to behave
  Has built in Field Generator
  Full Duplex – broadcasts at 433Mhz and listens
    on 916Mhz
Field Generator
  Sends out signal and wakes up active tags
  Transmit range configurable to match zone
  Periodic or sensor based activation
Tags
  Various types to match application
  Can have onboard LED and/or Alarm
  Smaller you go, the shorter the range
  Can track temperature and tampering

## Slide 4: Active Tags
Mini-Tag
  100’ transmit range
  Small parts
Compact Tag
  145’ transmit range
  Monitors, wheelchairs, etc.
Card Tag
  Thin footprint - ideal for access control badge
  280’ transmit range
Wristband tag
  Access control
  Monitor Temperature
  Tamper proof

## Slide 5: Active Technology - Modes of Operation
Beacon mode
  Tag wakes up at given intervals and reports “I’m here”.
Periodic mode
  Reader or Field Generator periodically transmits a command to Tag. Tag responds back to Reader.
  User-configurable ON and OFF times.
Trigger mode
  Reader or Field Generator calls a Tag when an external event happens, e.g., motion sensor activation.
User mode
  User initiates Tag call from computer.
  Can call all tags, specific tag type, specific tag ID range, or specific tag ID and type.

## Slide 6: Monitoring Floor with Different Modes
Periodic Mode
Beacon Mode
Trigger Mode

## Slide 7: Active Tag Applications
Hands-free Access Control
Patient / Employee Monitor
Equipment Tracking
Automatic In-room Billing
Supplies Inventory Control
Quarantine

## Slide 8: Hands-free Access Control
With the long, adjustable range of active tags, active RFID systems can read tags within several feet of any door.
Active tags do not have to be manually placed close to the door Reader like passive tags.
Possible applications:
  Control entry through locked doors to secured areas such as nurseries and labs.
  Only allow newborns to leave with authorized people – dual tag validation.
  Prevent Alzheimer’s and dementia patients from exiting hospital grounds.
  Control employee-only doors and after-hours entries.

## Slide 9: Patient / Employee Monitoring
The high power of active tags allow them to be reliably read when passing by Readers.
Possible applications:
  Monitoring patients and employees throughout entire hospitals.
  Locating patients and employees in any room or hallway.
  Recording the movement of newborns and Alheimer’s patients throughout a facility.

## Slide 10: Equipment Tracking
Active tags not only provide a unique ID to medical equipment, but can be used to track movement as well.
Possible applications:
  Track movement and usage of equipment.
  Locate missing equipment, e.g., system can read all equipment in several storage rooms simultaneously.

## Slide 11: Automatic In-room Billing
Active tags provide an accurate history of time spent in each patient’s room.
Billing hours applied to doctors’ times and specific medical equipment usage.
Doctors and other specialists can have a reliable account of exactly how much time is spent per patient.
Heart monitors, drug carts, wheelchairs and other equipment time can be automatically billed to the correct patient.

## Slide 12: Example Active RFID Application
Asset Management
Identify tagged equipment using beacon mode.
Each tag periodically transmits its unique ID to Reader.
If tag does not “report in” by specified time, system will generate alarm.
RFID Active Reader

## Slide 13: Zoning Example
Track movement from zone to zone
Detect movement with motion sensor activation (trigger mode).
Locate tags per zone
Find tagged goods instantly throughout entire facility per zone by manually activating each Reader (user mode).
Automatic inventory control
Read all tags periodically for real-time inventory control (periodic mode).
RFID Active Reader
Install Readers in ceilings at Zone centers.

## Slide 14: Thank You
Your Total RFID Solutions Provider